Town of Trumbull, Connecticut

REQUEST FOR PROPOSAL, CONDITIONS, Specifications,

special provisions and drawings

LOTCIP No. L144-0002

RFP# 6333

STROBEL ROAD RECONSTRUCTION PROJECT

PROPOSAL SUBMITTAL: MARCH 29, 2019 @ 2 pm

PREPARED FOR THE TOWN OF TRUMBULL BY:

Tighe&Bond

Consulting Engineers

1000 Bridgeport Avenue

Suite 320

Shelton, CT 06484

(203)712-1100)

www.tighebond.com

TABLE OF CONTENTS

| Section | Title | Number of Pages |
| --- | --- | --- |
|  | NOTICE TO PROPOSERs (Legal Notice) | 1 |
|  | GENERAL INSTRUCTIONS | 1-36 |
|  | STATEMENT OF QUALIFICATIONS |  |
|  | REFERENCES |  |
|  | PROPOSED SUBCONTRACTORS |  |
|  | PROPOSAL |  |
|  | BID FORM |  |
| 00520 | Agreement | 6 |
|  | BID BOND (EJCDC C340) | 3 |
|  | Commission on Human Rights and Opportunity Contract Compliance Regulations – Notification to Bidders |  |
|  | Certificate of Compliance with Connecticut General State Section 31-57b |  |
|  | PERFORMANCE BOND (EJCDC C610) | 3 |
|  | PAYMENT BOND (EJCDC C615) | 3 |
|  | Town of Trumbull General Specifications | 1-26 |
|  | Construction Contracts – Required Contract Provisions | 1-27 |
| 1 | Title VI of the Civil Right Act of 1964/Nondiscrimination Requirements |  |
| 2 | Contractor Work Force Utilization/Specific Equal Employment Opportunity |  |
| 3 | Contract Wage Rates |  |
| 4 | Americans with Disabilities Act of 1990, as amended |  |
| 5 | Connecticut Statutory Labor Requirements |  |
| 6 | Tax Liability – Contractors’ Exempt Purchase Certificate (CERT-141) |  |
| 7 | Executive Order (State of CT) |  |
| 8 | NonDiscrimination Requirement (pursuant to section 4a-60 and 4a-60a of the Connecticut General Statues, as revised) |  |
| 9 | Whistleblower Provision |  |
| 10 | Connecticut Freedom of Information Act |  |
| 11 | Service of Process |  |
| 12 | Substitution of Securities |  |
| 13 | Health Insurance Portability and Accountability Act of 1996 (HIPAA) |  |
| 14 | Forum and Choice of Law |  |
| 15 | Summary of State Ethics Law |  |
| 16 | Audit and Inspection of Plants, Places of Business and Records |  |
| 17 | Campaign Contribution Restriction |  |
| 18 | Tangible Personal Property |  |
| 19 | Bid Rigging and/or Fraud – Notice to Contractor |  |
| 20 | Consulting Agreement Affidavit |  |
|  | Exhibit A - Title VI Contractor Assurances (page 13) |  |
|  | Exhibit B - Contractor Work Force Utilization / Equal Employment Opportunity (page 14) |  |
|  | Exhibit C – Health Insurance Portability and Accountability Act of 1996 (HIPAA) (page17) |  |
|  | Exhibit D - Campaign Contribution Restriction (page 25) |  |
|  | Exhibit E – State Wage Rates (attached at the end of the Project Manual) |  |
|  | SPECIAL PROVISIONS (Included in this Document) |  |
|  | NOTICE TO CONTRACTOR – CONTRACT TIME AND LIQUIDATED DAMAGES | 1 |
|  | NOTICE TO CONTRACTOR – COORDINATION WITH EXISTING UTILITY COMPANIES | 4 |
|  | NOTICE TO CONTRACTOR – EXISTING UTILITIES | 1 |
|  | NOTICE TO CONTRACTOR – POTENTIAL MODIFIED AWARD SCHEDULE | 1 |
|  | NOTICE TO CONTRACTOR – CONTRACTOR TRAINING REQUIREMENT FOR 10-HOUR OSHA CONSTRUCTION SAFETY AND HEALTH COURSE | 1 |
|  | NOTICE TO CONTRACTOR – VEHICLE EMISSIONS | 2 |
|  | NOTICE TO CONTRACTOR – SECTION 4.06 AND M.04 MIX DESIGNATION EQUIVALENCY | 3 |
|  | NOTICE TO CONTRACTOR – SUPERPAVE DESIGN LEVEL INFORMATION | 1 |
| Section 1.08 | SECTION 1.08 – PROSECUTION AND PROGRESS | 4 |
| Section 2.86 | DRAINAGE TRENCH EXCAVATION, ROCK IN DRINAGE TRENCH EXCAVATION | 4 |
| Section 4.06 | SECTION 4.06 – BITUMINOUS CONCRETE | 24 |
| Section 5.86 | SECTION 5.86 – CATCH BASINS, MANHOLES AND DROP INLETS | 4 |
| Section 6.86 | DRAINAGE PIPES, DRAINAGE PIPE ENDS | 4 |
| Section M.04 | BITUMINOUS CONCRETE MATERIALS | 23 |
| ITEM #0202216A | EXCAVATION AND REUSE OF EXISTING CHANNEL BOTTOM MATERIAL | 3 |
| ITEM #0202217A | SUPPLEMENTAL STREAMBED CHANNEL MATERIAL | 2 |
| ITEM #0202451A | TEST PIT EXCAVATION | 1 |
| ITEM #0203001A | STRUCTURE EXCAVATION EARTH (complete) FOR CULVERT | 1 |
| ITEM #0203100A | STRUCTURE EXCAVATION ROCK (complete) FOR CULVERT | 1 |
| ITEM #0219011A | CATCH BASIN SEDIMENT FILTER | 1 |
| ITEM #0403869A | COLD RECLAIMED ASPHALT PAVEMENT | 4 |
| ITEM #0403871A | HANDLING COLD RECLAIMED ASPHALT PAVEMENT | 1 |
| ITEM #0406999A | ASPHALT ADJUSTMENT COST | 1 |
| ITEM #0601082A | (7’X7’) PRE-CAST CONCRETE BOX CULVERT | 5 |
| ITEM #0601109A | CLASS A CONCRETE FOR RETANING WALLS AND HEADWALLS | 1 |
| ITEM #0602910A | DRILLING HOLES AND GROUTING DOWELS | 2 |
| ITEM #0603591A | WATER MAIN BRACKET | 1 |
| ITEM #0605003A | MASONRY FACING FOR RETAINING WALL and CULVERT WINGWALLS | 2 |
| ITEM #0707009A | MEMBRANE WATERPROFFING | 1 |
| ITEM #0950001A | RESET BELGIUM BLOCK APRON | 1 |
| ITEM #0950005A | RESET STONE CURB | 1 |
| ITEM #0950019A | TURF ESTABLISHMENT - LAWN | 1 |
| ITEM #0969060A | CONSTRUCTION FIELD OFFICE, SMALL | 8 |
| ITEM #0971001A | MAINTENANCE AND PROTECTION OF TRAFFIC | 26 |
| ITEM #0970006A | TRAFFICPERSON (MUNICIPAL POLICE OFFICER) | 3 |
| ITEM #0970007A | TRAFFICPERSON (MUNICIPAL POLICE OFFICER) | 3 |
| ITEM #0980001A | CONSTRUCTION STAKING | 1 |
| ITEM #1002202A | TRAFFIC CONTROL FOUNDATION – MAST ARMI | 12 |
| ITEM #1017032A | SERVICE (METERED) | 2 |
| ITEM #1102002A | 8’ ALUMINUM PEDESTAL | 4 |
| ITEM #1104033A | 40’ STEEL MAST ARM ASSEMBLY | 14 |
| ITEM #1104037A | 45’ STEEL MAST ARM ASSEMBLY | 14 |
| ITEM #1105103A | 1 WAY, 5 SECTION MAST ARM TRAFFIC SIGNAL | 4 |
| ITEM #1106001A | 1 WAY PEDESTRIAN SIGNAL POLE MOUNTED | 2 |
| ITEM #1106003A | 1 WAY PEDESTRIAN SIGNAL PEDESTAL MOUNTED | 2 |
| ITEM #1107011A | ACCESSIBLE PEDESTRIAN SIGNAL AND DETECTOR (TYPE A) | 3 |
| ITEM #1108578A | FULL ACTUATED CONTROLLER 8 PHASE (MODIFIED) | 14 |
| ITEM #1111407A | CAMERA VIDEO DETECTION SYSTEM | 12 |
| ITEM #1111600A | EXTENSION BRACKET | 7 |
| ITEM #1112286A | 360 DEGREE CAMERA ASSEMBLY | 7 |
| ITEM #1112287A | 360 DEGREE VIDEO DETECTION PROCESOR | 7 |
| ITEM #1113725A | 23 AWG 4 TWISTED PAIR CATEGORY 6 CABLE | 7 |
| ITEM #1112288A | IP VIDEO DETECTION CAMERA ASSEMBLY | 3 |
| ITEM #1118051A | TEMPORARY SIGNALIZATION (SITE NO.1) | 5 |
| ITEM #1206023A | REMOVAL AND RELOCATION OF EXISTING SIGNS | 1 |
| ITEM #1208931A | SIGN FACE – SHEET ALUMINUM (TYPE IX RETROREFLECTIVE SHEETING | 2 |
| ITEM #1208932A | SIGN FACE – SHEET ALUMINUM (TYPE IV RETROREFLECTIVE SHEETING | 2 |

ATTACHMENTS

CONNECTICUT STATE PREVAILING WAGE RATES

DRAWINGS (Included in this Document)

| LIST OF DRAWINGS |
| --- |
|  | Cover Sheet |
| C0.1 – C0.2 | Sheet Index Plan |
| C1.0 | General Notes, Abbreviations, Legend and Boring Logs |
| C2.0 | Typical Sections |
| C3.0 – C3.3 | Daniels Farm Roadway Plans |
| C3.1 | Strobel Roadway Plans |
| C3.4 – C.17 | Strobel Roadway Plans |
| C4.0 | Daniels Farm Roadway Profiles |
| C4.1 - C4.8 | Strobel Roadway Profiles |
| C5.0 | Existing Conditions Culvert Plan |
| C5.1 | Structural Notes and Details |
| C5.2 | Culvert Layout and Elevation Plan |
| C5.3 | Culvert Sections |
| C5.4 | Water Handling Plan |
| C5.5 | Details |
| C6.0 – C6.2 | Retaining Wall Plan – Wall No. 1 |
| C6.3 | Retaining Wall Plan – Wall No. 2 |
| C6.4 – C6.5 | Retaining Wall Plan – Wall No. 3 |
| C7.0 – C7.1 | Traffic Control Signal Plans |
| C8.0 – C8.2 | Details |
| C8.3 – C8.22 | CONNDOT Details |
| C9.0 – C9.6 | Daniels Farm Road Cross-Sections |
| C9.7 – C9.67 | Strobel Road Cross-Sections |
| C8.3 – C8.22 | CONNDOT Details |
| TTC-001 | Strobel Road Phase 1 Detour Plan |
| TTC-002 | Strobel Road Phase 2 Detour Plan |
| TTC-003 | Strobel Road Phase 3 Detour Plan |
| TCC-004 | Temporary Traffic Control Signal Plan |

Notice to Proposers

Town of Trumbull

TOWN ENGINEERING

REQUEST FOR PROPOSALS

STROBEL ROAD RECONSTRUCTION PROJECT

LOTCIP No. L144-0002

RFP # 6333	DUE:  MARCH 29, 2019 at 2:00PM

Sealed proposals for the Strobel Road Reconstruction Project will be received at the office of the Purchasing Agent, 5866 Main Street, Trumbull, Connecticut, on or before the date indicated above, at which time all proposals received will be opened and read aloud.

Proposal documents are available from the Purchasing Department website www.trumbull-ct.gov and also on the State Contracting Portal www.das.ct.gov/portal   and may be obtained (at a cost to you) from Digiprint, 909 Main Street. Stratford, CT 06615. The consulting engineer for this project is: Tighe and Bond, 1000 Bridgeport Ave., Shelton, CT 203.712.1100.

Proposers shall comply with State mandated Guidelines if and shall comply with Equal Opportunity Employment Practices, and Safety and Health Regulations.

This Contract is subject to State set-aside and contract compliance requirements.

SBE/MBE requirements shall be in accordance with Commission on Human Rights and

Opportunity Contract Compliance Regulations (CHRO).

Bid Security is required in the amount of ten percent (10%) of the base proposal and shall be in the form of a Certified Check or Bid Bond.  A Performance and Payment Bond in the full amount (100%) of the contract is required and shall be included in the Base Proposal.  No oral, telephone or telegraphic responses shall be considered.  A proposer may not withdraw a proposal within ninety (90) days of the proposal opening.

The Town of Trumbull reserves the right to waive and/or reject any and all proposals or any part thereof, waive the information in the proposal process, and reject any unqualified proposals, or accept any proposal or part thereof, deemed to be in the best interest of the Town of Trumbull.

Kevin Bova

Purchasing Agent

Town of Trumbull

TOWN ENGINEERING

REQUEST FOR PROPOSALS

STROBEL ROAD RECONSTRUCTION PROJECT

LOTCIP No. L144-0002

RFP # 6333	DUE:  MARCH 29, 2019 at 2:00PM

GENERAL INSTRUCTIONS

The Town of Trumbull, (hereinafter referred to as Town or Owner), through the office of the Purchasing Agent, will accept sealed proposals for the STROBEL ROAD RECONSTUCTION PROJECT in the Town of Trumbull in accordance with the specifications and requirements detailed in this request.   All qualified and interested parties (hereinafter referred to as proposer, bidder, contractor or supplier) are invited to submit proposals under the terms and conditions set forth as follows:

This RFP is not a contract offer, and no contract exists until a written contract is signed by the Town and the successful proposer. It’s the sole responsibility of the contractor/ vendor to check the Towns website for any addendum.

1.	PREPARATION FOR PROPOSALS

Bids shall be submitted by using the enclosed BID PROPOSAL FORM that accompanies this request.  Submit one (1) ORIGINAL and Two (2) EXACT COPY.  Bidders should submit bids in a clear, concise and legible manner to permit proper evaluation of responsive bids.

An original and Two (2) exact copies of each Proposal shall be submitted in a sealed envelope, and addressed to: Purchasing Agent, Town of Trumbull, in a sealed envelope and plainly marked on the outside as “STROBEL ROAD RECONSTUCTION PROJECT”.  The envelope shall bear on the outside the name of the proposer and address.  No oral, telephone or telegraphic responses will be considered.  Proposals received after the advertised time and date due shall not be opened or considered.  The Town reserves the right to communicate with any or all of the proposers to clarify the provisions of Proposals.  The Town further reserves the right to request additional information from any proposer at any time after proposals are opened

2.	PROPOSAL SUBMISSION

  - Proposals are to be completed (unless directed otherwise in the specifications), printed, signed by an authorized agent, and sealed in an envelope (including all official literature, brochures, etc., which support this request) and addressed as follows:

BID 6333 STROBEL ROAD RECONSTUCTION PROJECT

Trumbull Town Hall – Attn: Kevin Bova, Purchasing Agent

5866 Main Street, Trumbull CT  06611

DUE: March 29, 2019 at 2 pm sharp

  - All Proposals must be made on the enclosed Proposal form.  All blank spaces for Proposal prices must be filled in, in ink or typewritten, and the proposal form must be fully completed and executed when submitted.  Please be advised that the person signing the formal proposal must be authorized by your organization to contractually bind your firm with regard to prices and related contractual obligations for the subject project

  - The party signing the formal proposal must be authorized by your organization to contractually bind your firm with regard to prices and related contractual obligations for the contractual period requested.

  - The Town reserves the right to correct, after proposer verification, any mistake in a proposal that is a clerical error, such as a price extension or decimal point error.

3.	PROPOSAL RESPONSE TIME

Responses to this request shall be received at the office of the Purchasing Agent, Town Hall prior to the advertised hour (noted above) of opening, at which time all proposals (total proposal amount only) shall be publicly opened and read aloud.  A proposer may withdraw a proposal at any time prior to the above scheduled date and time.  Any proposal received after the above scheduled date and time shall not be considered or opened.  No proposer may withdraw a proposal within ninety (90) days after the actual proposal opening.

4.	TOWN OPTIONS - Omitted

5.	TAX EXEMPT

The Town of Trumbull is exempt from the payment of taxes imposed by the Federal Government and/or State of Connecticut.  Such taxes must not be included in the proposal price.  The Town of Trumbull Tax Exempt number is 05-010 31-000.

6.	SPECIFICATIONS

- If quoted materials and/or equipment do not meet or better the attached specifications on ALL points, the proposer must note ALL exceptions as separate attachments to their formal response; otherwise, it will be presumed that the proposal is in accordance with all specifications requested herein. Each Bidder will be held responsible to have studied the Specifications, visit the site (if necessary), regarding the proposed work, satisfied itself regarding all existing conditions and measurements, and to have included in the proposal an amount sufficient to cover all work.

- Should any Bidder find discrepancies in the Specifications, or be in doubt as to the exact meaning, notify the Town at once.  The Town may then at their option, issue Addenda clarifying same.  The Town shall not be responsible for oral instructions or misinterpretations of Specifications.

- The Town reserves the right to issue Addenda at any time prior to the Bid Opening.  All such Addenda become, upon issuance part of the Specification.  Each Bidder shall cover such Addenda in the proposal and shall acknowledge receipt of same on the blank provided therefore.  It is the bidders’ responsibility to access the Town’s website or contact the Town for any addenda that may be issued in conjunction with this bid.

- The Town reserves the right to require any or all Bidders to submit statements as to previous experience in performing comparable work; and as to financial and technical organizations and resources available for this work.  The mere opening and reading aloud of a bid shall not constitute or imply the Town’s acceptance of the suitability of a Bidder or the bid, nor shall possession of Drawings or Specifications constitute an invitation to bid.  The competency and responsibility of Bidders as well as the number of working days required for completion will be considered in making an award.

7.	INQUIRIES & ADDENDUMS

a)	All technical inquiries regarding this request shall be answered up to the close of business on March 22 2019, 2019 after which time no additional questions will be accepted to

William Maurer– Trumbull Town Engineer (203-452-5056) wmaurer@trumbull-ct.gov

and a copy to Fred Mascia at Tighe & Bond, Inc., (203-712-1100), ajmascia@tighebond.com.

All other questions may be directed to Kevin J. Bova Purchasing Agent (203.452.5042) kbova@trumbull-ct.gov.

- All technical inquiries regarding this request shall be answered up to the close of business on March 22, 2019 after which time no additional questions will be accepted. Answers to questions the Town deems to be in the interest of all proposers will be made available in writing, email or by Fax as appropriate to all proposers or posted as an addendum on the Town web site.

- to communicate with any or all the proposers to clarify the provisions of this request; the Town further reserves the right to request additional information from any proposer at any time after proposals are opened.

- It is the sole responsibility of a proposer to verify any addendums that may have been issued relating to this request prior to submission of a proposal.  Any notice of addendum shall be published on the Town website (www.trumbull-ct.gov ) in the Purchasing Department Section (Bid Notices).  Failure to submit a response that does not address any changes or addendums may result in a disqualification of a proposal submission.

8.	ASSIGNMENT OF RIGHTS, TITLES, AND INTERESTS

Any assignment or subcontracting by a proposer, bidder, supplier, or contractor for work to be performed, or goods and/or services to be provided, in whole or in part, and any other interest in conjunction with a Town procurement shall not be permitted without the express written consent of the Town of Trumbull.

9.	HOLD HARMLESS CLAUSE

The Contractor agrees to indemnify, hold harmless and defend the Town from and against any and all liability for loss, damage or expense which the Town may suffer or for which the Town may be held liable by reason of injury, including death, to any person or damage to any property arising out of or in any manner connected with the operations to be performed under this request, whether or not due in whole or in part of any act, omission or negligence of the Owner or any of his representatives or employees.

10.	WORK REGULATIONS, STANDARDS AND FEDERAL AND STATE PREVAILING WAGE

- All work activities performed in association with this request must be performed and completed for the Town in accordance with current Federal State and Local regulations.  All services performed shall also conform to the latest OSHA standards and/or regulations.

- Applicable laws and regulations relating to employment practices, nondiscrimination, safety and health regulations shall be adhered to by the contractor.  The contractor shall be responsible for “Certified Statements of Compliance” regarding Prevailing Wages.  Contractor shall also collect and submit four (4) Certified “Statements of Compliance” from any sub-contractors. If the low qualified low bidder is chosen and is not over 100,000.00 then prevailing wages will NOT apply.

11.	INSURANCE

The successful proposer shall provide the Town Purchasing Agent with a Certificate of Insurance before work commences.  The Town shall be named as an additional insured with an Insurance Company licensed to write such insurance in Connecticut, against the following risks and in not less than those listed in the table below:

Workers’ Compensation – With Respect to all operations the Contractor performs and all those performed for it by subcontractors, The Contractor shall carry, and require each subcontractor to carry, Worker’s Compensation insurance as required by the laws of the State of Connecticut.

Employer’s liability insurance shall be provided in amounts no less than $100,000 per accident for bodily injury by accident; $100,000 policy limit by disease and $100,000 per employee for bodily injury by disease.

| Commercial General Liability | Minimum Single Occurrence Amount | Minimum Annual Aggregate Amount |
| --- | --- | --- |
| Bodily Injury Liability | $2,000,000 | $5,000,000 |
| Property Damage Liability | $1,000,000 | $5,000,000 |
| Personal Injury Liability | $1,000,000 | $5,000,000 |
| Comprehensive Auto Liability (Including coverage of owned, non-owned & rented vehicles) | Minimum Single Occurrence Amount | Minimum Annual Aggregate Amount |
| Bodily injury to or death of all persons | $2,000,000 | No aggregate limitation |
| Injury to or destruction of property | $2,000,000 | No aggregate limitation |

The insurance policy must contain the additional provision wherein the company agrees that Thirty (30) days prior to termination, expiration, cancellation or reduction of the insurance afforded by this policy with respect to the contract involved, written notice will be served by registered mail to the Purchasing Agent, Town of Trumbull.

Additionally, the successful proposer (Contractor) shall provide adequate statutory Workmen’s Compensation Insurance for all labor employed on this project, and comprehensive General Public Liability Insurance (Coverage “B”)

The successful proposer (Contractor) and each Subcontractor agree that their insurance carriers waive subrogation against the Town, its agents or employees with respect to any loss covered by the Contractor’s and each Subcontractor’s insurance.

12.	CONFLICT OF INTEREST

Public officials shall be prohibited from receiving any town work procured through a public

Bid or bid waived process so as to avoid any appearance of impropriety or conflict of interest;

And; Public officials cannot circumvent the intent of this ordinance by receiving town work

Through a bid waiver, as proscribed by the Trumbull Town Charter.

13.	PROPOSAL, PERFORMANCE AND PAYMENT BONDS

- A Bond payable to the Owner must accompany each Proposal for ten (10%) percent of the total amount of the Proposal.  As soon as the Proposal prices have been compared, the Owner will return the bonds of all except the three lowest responsible Proposals.  When the Agreement is executed, the bonds of the two remaining unsuccessful Proposers will be returned.  The Proposal Bond of the successful Proposer will be retained until the Payment Bond and Performance Bond have been executed and approved, after which it will be returned.  A certified check may be used in lieu of a Proposal (Bid) Bond.

- A Performance Bond and a Payment Bond, each in the amount of 100 percent (100%) of the Contract Price, with a corporate surety approved by the Owner, will be required for the faithful performance of the contract.  Attorneys-in-fact who sign the Bid Bonds or Payment Bonds and Performance Bonds must file with each bond, a certified and effective dated copy of their power of attorney.

- The party to whom the contract is awarded will be required to execute the Agreement and obtain the Performance Bond and Payment Bond within ten (10) calendar days from the date when Notice of Award is delivered to the Proposer. The Notice of Award shall be accompanied by the necessary Agreement and Bond forms. In case of failure of the Proposer to execute the Agreement, the Owner may, at his option, consider the Proposer in default, in which case the Bid Bond accompanying the proposal shall become the property of the Owner.

- The Owner, upon receipt of acceptable Performance Bond, Payment Bond and Agreement signed by the Contractor, shall sign the Agreement and return to the Contractor an executed duplicate of the Agreement within a reasonable period of time. The returned executed Agreement by the Owner to the Contractor shall be accompanied with a Notice to Proceed.

- The Contractor shall secure a maintenance bond with a company which shall have been approved by the Attorney of the Town of Trumbull, guaranteeing his work in all phases of construction for a period of two (2) years from the date of acceptance by the Town which shall also cover all damages due to trench settlement.

- The face value of the maintenance bond shall be as follows: 5% of the base bid of contracts over $50,000.

14.	work schedule

The Town anticipates Work shall begin on or about July 6, 2019 and be completed in accordance with the requirements of the “Notice to the Contractor -Contract Time and Liquidated Damages”.

15.	LOWEST RESPONSIBLE PROPOSAL

- The Town shall determine the “lowest responsible qualified proposer” on the basis of the Proposer submitting the lowest “Total Proposal”, responsiveness of his Technical Proposal; and demonstrating a history of the ability and integrity necessary to perform the required work; and certifying that it shall perform the work in accordance with the specifications.

- Proposals will be compared on the basis of the “Total Proposal” of the items listed in the Proposal and on basis of the Proposer’s experience and competence.

- If the Lowest Total Proposal exceeds the amount of funds available for the project, the Town reserves the right to increase or decrease any class, item or part of the work.  After determining the “lowest responsible qualified proposer”, the Town will issue a Notice of Award to the successful Proposer.

- The Proposer designated by the Town as the “lowest responsible qualified proposer” to whom the contract is awarded shall execute the Contact and submit the following documents:

    - Performance Bond

    - Labor, Payment and Materials Bond

    - Copy of valid license issued by the State of Connecticut, Department of Consumer Protection.

- In the event that the lowest responsible qualified proposer fails to execute the Contact and/or fails to provide the required documents within the time period prescribed, the Town, at its option, may consider the lowest responsible qualified proposer to be in default, in which case the Bid Guarantee shall become the property of the Town.

16. LIQUIDATED DAMAGES

Each work assignment must be completed within 425 days after town issuing Letter to proceed. Contractor further agrees to pay as liquidated damages, the sum of ($2,200) two thousand two hundred dollars for each consecutive calendar day thereafter from letter to Proceed

17. DELIVERY TIME IS OF THE ESSENCE - Omitted

18. STATEMENT OF QUALIFICATIONS AND REFERENCES

Bidders shall complete and submit the “Statement of Qualifications” section of this request along with the References form. The Town and Engineering Department may make such investigations as necessary and it deems appropriate to determine the qualifications of the proposer to perform the work required. If the Town is not satisfied that the proposer is properly qualified, the Town along with Engineering Department reserves the right to reject the proposal of said proposer.

19.	Miscellaneous

- All Contractors must develop a complete and thorough schedule which demonstrates that the Contractor will be able to complete the project in a timely fashion.

- Selected proposer agrees to warranty all work completed for this requirement.

- The Town may make such investigations as necessary and it deems appropriate to determine the qualifications of the proposer to perform the work required.  Each proposer shall submit a Statement of Bidder Qualifications.  If the Town is not satisfied that the proposer is properly qualified, the Town reserves the right to reject the proposal of said proposer.

- All material testing and material certification shall be in accordance with State and LOTCIP requirements.

- All closeout documents must be in accordance with State and LOTCIP requirements.

- The Contractor will coordinate with State directly for CHRO requirements (Commission on Human Rights and Opportunity Contract Compliance Regulations).

20.    AWARD AND AUTHORITY

The Purchasing agent from Town Hall on will issue notification of award in writing along with Standard contract and a Purchase order. THE TOWN RESERVES THE RIGHT TO ELIMINATE ANY OR ALL ALTERNATE ITEMS. LOW BIDDER WILL THEN BE BASED ON THE PROPOSAL OF REMAINING BASE BID AND / OR EITHER ALTERNATE.

ALL Original Invoices, submittals waiver of liens and certified payroll TO BE SENT TO:

ENGINEERING DEPARTMENT

ATT: William Maurer–

5866 MAIN STREET

TRUMBULL CT 06611

21.    STATE SET-ASIDE

- The contractor who is selected to perform this State project must comply with CONN. GEN.STAT. §§ 4a-60, 4a-60a, 4a-60g, and 46a-68b through 46a-68f, inclusive, as amended by June 2015 Special Session Public Act 15-5.

- State law requires a minimum of twenty-five (25%) percent of the state-funded portion of the contract for award to subcontractors holding current certification from the Connecticut Department of Administrative Services ("DAS") under the provisions of CONN. GEN. STAT. §4a-60g. (25% of the work with DAS ce11ified Small and Minority owned businesses and 25% of that work with DAS ce11ified Minority, Women and/or Disabled owned business) The contractor must demonstrate good faith effort to meet the 25% set-aside goals.

- Contractor will coordinate with the State directly for Commission on Human Rights & Opportunity Contract Compliance regulations (CHRO)

- For municipal public works contracts and quasi-public agency projects, the contractor must file a written or electronic non-discrimination certification with the Commission on Human Rights and Opportunities.  Forms can be found at:

http://www.ct.gov/opm/cwp/view.asp?a=2982&g=390928& opmNav_GID=1806

Forms and Reports For Construction Contractors

- Checklist for Contractors on Municipal Public Works Contracts

- Affirmative Action Plan Format

- Set Aside Plan Format

- Sample AA/EOE Policy Statement

- Instructions for Filing Forms

- Minority Workforce Utilization Report (CHRO CC257 AND CC 257a)

- Cumulative Minority Workforce Utilization Report (CHRO CC257b)

- Small Contractor and MBE Status Report (CC258a)

- Monthly     Materials Consumption Report (CHRO CC259)

- Map of CT Metropolitan Statistical Areas

- Links to maps for download in various formats

Town of Trumbull

TOWN ENGINEERING

REQUEST FOR PROPOSALS

STROBEL ROAD RECONSTRUCTION PROJECT

LOTCIP No. L144-0002

RFP # 6333	DUE:  MARCH 29, 2019 at 2:00PM

STATEMENT OF QUALIFICATIONS (To be submitted with proposal)

Submitted by:

Name of Organization _____________________________________________________________

Name of Individual _____________________________________________________________

Title _____________________________________________________________

Address _____________________________________________________________

_____________________________________________________________

_____________________________________________________________

Telephone _____________________________________________________________

Submitted to:

Name _____________________________________________________________

Address _____________________________________________________________

_____________________________________________________________

_____________________________________________________________

Telephone _____________________________________________________________

Project Name and Description (if applicable)

_____________________________________________________________

_____________________________________________________________

Contractor's General Business Information

Check If:

Corporation Partnership Joint Venture Sole Proprietorship

If Corporation:

a. Date and State of Incorporation

_____________________________________________________________________________

_____________________________________________________________________________

b. List of Executive Officers

Name Title

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

If Partnership:

a. Date and State of Organization

_____________________________________________________________________________

b. Names of Current General Partners

_____________________________________________________________________________

c. Type of Partnership

General Publicly Traded

Limited Other (describe):______________________________________

If Joint Venture:

a. Date and State of Organization

_____________________________________________________________________________

b. Name, Address and Form of Organization of Joint Venture Partners: (Indicate managing partner by an asterisk*)

_____________________________________________________________________________

_____________________________________________________________________________

If Sole Proprietorship:

a. Date and State of Organization

_____________________________________________________________________________

_____________________________________________________________________________ b. Name and Address of Owner or Owners

_____________________________________________________________________________

_____________________________________________________________________________

1. On Schedule A, attached, list major engineered construction projects completed by this organization in the past five (5) years. (If a joint venture list each participant's projects separately).

2. On Schedule B, attached, list current projects under construction by this organization. (If joint venture, list each participant's projects separately).

3. Name of surety company and name, address, and phone number of agent.

_____________________________________________________________________________

_____________________________________________________________________________

4. Is your organization a member of a controlled group of corporations as defined in I.R.C. Sec. 1563?

Yes___		 No ____

If yes, show names and addresses of affiliated companies.

_____________________________________________________________________________

_____________________________________________________________________________

5. Furnish on Schedule C, attached, details of the construction experience of the principal individuals of your organization directly involved in construction operations.

6. Has your organization ever failed to complete any construction contract awarded to it? 
Yes___		 No ____

If yes, describe circumstances on attachment.

7. Has any Corporate officer, partner, joint venture participant or proprietor ever failed to complete a construction contract awarded to him or her in their own name or when acting as a principal of another organization?

Yes___		 No ____

If yes, describe circumstances on attachment.

8. In the last five years, has your organization ever failed to substantially complete a project in a timely manner?

Yes___		 No ____

If yes, describe circumstances on attachment.

I hereby certify that the information submitted herewith, including any attachment is true to the best of my knowledge and belief.

Name of Organization: _______________________________________

By: _______________________________________

Title: _______________________________________

Dated: _______________________________________

Town of Trumbull

TOWN ENGINEERING

REQUEST FOR PROPOSALS

STROBEL ROAD RECONSTRUCTION PROJECT

LOTCIP No. L144-0002

RFP # 6333	DUE:  MARCH 29, 2019 at 2:00PM

Schedule A: Prior Experience (Copy Additional Pages as Needed)

| Project | Owner | Design Professional | Contract Price | Amount Completed | Date of Scheduled Completion |
| --- | --- | --- | --- | --- | --- |

Schedule B: Current Experience (Copy Additional Pages as Needed)

| Project | Owner | Design Professional | Contract Price | Amount Completed | Date of Scheduled Completion |
| --- | --- | --- | --- | --- | --- |

Schedule C: Personnel (Copy Additional Pages as Needed)

| Name | Position | Date of Hire | Date Started in Construction | Prior Positions & Construction Experience |
| --- | --- | --- | --- | --- |

Town of Trumbull

TOWN ENGINEERING

REQUEST FOR PROPOSALS

STROBEL ROAD RECONSTRUCTION PROJECT

LOTCIP No. L144-0002

RFP # 6333	DUE:  MARCH 29, 2019 at 2:00PM

###### REFERENCES

## (To be submitted with proposal – attach additional pages as necessary)

### List references for similar services provided for at least Four (4) clients in the past five (5) years (attach any other client references if desired).  PLEASE NOTE IT IS THE TOWN’S INTENT TO COMMUNICATE WITH THE REFERENCES LISTED HEREIN.

CLIENT 1:

Organization Name: ________________________________________________

Contact Name:	__________________________________________ Phone: ___________________________

Service Dates: _____________________________________________________

Project(s):   ___________________________________________________________________________________

CLIENT 2:

Organization Name: ________________________________________________

Contact Name:	__________________________________________ Phone: ___________________________

Service Dates: _____________________________________________________

Project(s):   ___________________________________________________________________________________

CLIENT 3:

Organization Name: ________________________________________________

Contact Name:	__________________________________________ Phone: ___________________________

Service Dates: _____________________________________________________

Project(s):   ___________________________________________________________________________________

CLIENT 4:

Organization Name: ________________________________________________

Contact Name:	__________________________________________ Phone: ___________________________

Service Dates: _____________________________________________________

Project(s):   ___________________________________________________________________________________

Town of Trumbull

TOWN ENGINEERING

REQUEST FOR PROPOSALS

STROBEL ROAD RECONSTRUCTION PROJECT

LOTCIP No. L144-0002

RFP # 6333	DUE:  MARCH 29, 2019 at 2:00PM

PROPOSED SUBCONTRACTORS

If none, write "None"__________________________________.

*Description of Work____________________________________________________

Proposed Subcontractor Name _____________________________________

Address________________________________________________________

*Description of Work____________________________________________________

Proposed Subcontractor Name _____________________________________

Address________________________________________________________

*Description of Work____________________________________________________

Proposed Subcontractor Name _____________________________________

Address________________________________________________________

*Description of Work____________________________________________________

Proposed Subcontractor Name _____________________________________

Address________________________________________________________

*Insert description of work and subcontractors' names as may be required.

This is to certify that the names of the above-mentioned subcontractors are submitted with full knowledge and consent of the respective parties.

The Proposer warrants that none of the proposed subcontractors have any conflict of interest as respects this contract.

Proposer	_____________________________________

(Fill in Name)

By ___________________________________________

(Signature and Title)

Town of Trumbull

TOWN ENGINEERING

REQUEST FOR PROPOSALS

STROBEL ROAD RECONSTRUCTION PROJECT

LOTCIP No. L144-0002

RFP # 6333	DUE:  MARCH 29, 2019 at 2:00PM

PROPOSAL

Proposal of ___________________________________________________ (hereinafter called "Proposer, Bidder"), organized and existing under the laws of the State of Connecticut, doing business as to the Engineering Department, Town of Trumbull, Connecticut (hereinafter called the “Owner").

In compliance with your Advertisement for Proposals, Proposer hereby proposes for the STROBEL ROAD RECONSTRUCTION PROJECT, in the Town of Trumbull, Connecticut together with all related incidental and appurtenant work as described in the specifications or outlined and/or shown on the exhibits. The work is to be done in strict accordance with the Specifications, Drawings and all Contract Documents, within the time set forth therein, and at the prices stated on the Proposal Schedule.

By submission of this Proposal, each Proposer certifies, that this Proposal has been arrived at independently, without consultation, communication, or agreement as to any matter relating to this Proposal with any other Proposer or with any competitor.

Proposer hereby agrees to commence work under this contract on or before a date to be specified in the “Notice to Proceed”, and to fully complete the Project within four hundred fifty-five (455) consecutive calendar days, excluding winter shutdown, thereafter.

Proposer further agrees to pay as liquidated damages, the sum of ($2,200.00) two thousand two hundred dollars for each consecutive calendar day thereafter till completion of the full contract as provided in the General Conditions.  Proposer further agrees that he will provide and sustain the required Bonds and Insurance Policies as required.

Proposer understands that the Owner reserves the right to reject any or all proposals and to waive any informality in the bidding.

Proposer agrees that this proposal shall be good and may not be withdrawn for a period of one hundred (120) calendar days after the scheduled closing time for receiving proposals.

Upon receipt of written notice of the acceptance of this proposal, proposer shall execute the formal contract attached within five (5) days and deliver a Surety Bond or Bonds as required in the General Conditions.  The Bid Security attached in the sum of___________________________________________________________Dollars ($________________) is to become the property of the Owner in the event the contract and bond are not executed within the time above set forth, as liquidated damages for the delay and additional expense to the Owner caused thereby.

________________________________________________			________________________________________________

Company Name												By (Signature)

________________________________________________			________________________________________________

Address														Print Name

_________________________________________________			________________________________________________

City-Town-Zip													Title

_________________________________________________			_________________________________________________

Date															Telephone/Fax

PROPOSAL – STROBEL ROAD RECONSTUCTION PROJECT (continued)

The undersigned hereby declares that in regard to all conditions affecting the work to be done and the labor and materials required, this proposal is based on his investigations and findings, and the Town of Trumbull and the Engineers and their officers, agents and employees shall not in any manner be held responsible for the accuracy of, or be bound by any estimates, borings, water or underground conditions relative to the proposed work, indicated in this or in the other contract documents; that no warranty or representation has been made by the Town of Trumbull or the Engineers or their officers, agents and employees as to subsurface soil or rock conditions, ground water, or other underground and similar conditions; nor has any representation or warranty been so made that the estimated quantities to be used for comparison of proposals will even approximate the actual quantities or materials and work which the Contractor may be required to furnish or perform.

BID FORM - Bidder will complete the Work in accordance with the Contract Documents for the following price(s):

| Strobel Road Reconstruction Project – LOTCIP Funds Participating Pay Items |
| --- |
| Item Number | Item Name and Unit Bid Prices Written in Words and Figures | Units | Estimated Quantity | Total Amount of Item (in figures) |
| 0201001 | Clearing and Grubbing, per LS, the price of: ($ ) | LS | 1 | $_______________ |
| 0202001 | Earth Excavation, per CY, the price of: ($ ) | CY | 4,567 | $_______________ |
| 0202100 | Rock Excavation, per CY, the price of: ($ ) | CY | 225 | $_______________ |
| 0202216A | Excavation and Reuse of Existing Channel Bottom Material, per CY, the price of: ($ ) | CY | 75 | $_______________ |
| 0202217A | Supplemental Streambed Channel Material, per CY, the price of: Two Thousand Five Hundred and 00/100 ( $2,500.00 ) | Est. | 1 | $2,500.00 |
| 0202451A | Test Pit Excavation, per CY, the price of: ($ ) | CY | 100 | $_______________ |
| 0202529 | Cut Bituminous Concrete Pavement, per LF, the price of: ($ ) | LF | 2,000 | $_______________ |
| 0203001A | Structure Excavation Earth (Complete) – For Culvert, per CY, the price of: ($ ) | CY | 600 | $_______________ |
| 02031001A | Structure Excavation Rock (Complete) – For Culvert, per CY, the price of: ($ ) | CY | 50 | $_______________ |
| 0204401 | Handling Water, per Lump Sum, the price of: ($ ) | LS | 1 | $_______________ |
| 0209001 | Formation of Subgrade, per SY, the price of: ($ ) | SY | 37,800 | $_______________ |
| 0210820 | Water Pollution Control, per Est., the price of: Twenty Thousand and 00/100 ( $20,000.00 ) | Est. | 1 | $20,000.00 |
| 0216000 | Pervious Structure Backfill, per CY, the price of: ($ ) | CY | 250 | $_______________ |
| 0219011 | Sediment Control System at Catch Basin, per Each, the price of: ($ ) | Each | 83 | $_______________ |
| 0219002 | Sedimentation Control Haybale System, per LF, the price of: ($ ) | LF | 300 | $_______________ |
| 0219003 | Sedimentation Control Filter Fabric Fence System, per LF, the price of: ($ ) | LF | 22,000 | $_______________ |
| 0286001.1 | Rock-In-Trench, per CY, the price of: ($ ) | CY | 200 | $_______________ |
| 0403869A | Cold Reclaimed Asphalt Pavement, per SY, the price of: ($ ) | SY | 34,476 | $_______________ |
| 0403871A | Handling Cold Reclaimed Asphalt Pavement, per SY, the price of: ($ ) | SY | 24,766 | $_______________ |
| 0406000 | Temporary Pavement, per SY, the price of: ($ ) | SY | 2,000 | $_______________ |
| 0406236 | Material for Tack Coat, per Gal, the price of: ($ ) | Gal | 1,735 | $_______________ |
| 0406170 | HMA S 1.0” (3”), per Ton, the price of: ($ ) | Ton | 6,450 | $_______________ |
| 0406712 | HMA S 0.375” (2”), per Ton, the price of: ($ ) | Ton | 4,000 | $_______________ |
| 0406606 | Material Transfer Vehicle, per Ton, the price of: ($ ) | Ton | 4,000 | $_______________ |
| 0406999A | Asphalt Adjustment Cost, per Est., the price of: Thirty-Three Thousand and 00/100 ($ 33,000.00 ) | Est. | 1 | $33,000.00 |
| 0586002.1 | Type “C” Catch Basin (4’ sump) 0-10’ deep, per Each, the price of: ($ ) | Each | 52 | $_______________ |
| 0586005.1 | Type “C” Catch Basin Double Grate Type 2 (4’ sump) 0-10’ deep, per Each, the price of: ($ ) | Each | 2 | $_______________ |
| 0586041.1 | Type “C-L” Catch Basin (4’ sump) 0-10’ deep, per Each, the price of: ($ ) | Each | 3 | $_______________ |
| 0586500.1 | Manhole 0-10’ deep, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 0586600 | Reset Catch Basin, per Each, the price of: ($ ) | Each | 77 | $_______________ |
| 0586650 | Reset Manhole (Sanitary), per Each, the price of: ($ ) | Each | 92 | $_______________ |
| 0586651 | Reset Manhole (Storm), per Each, the price of: ($ ) | Each | 20 | $_______________ |
| 0586703 | Convert Catch Basin to Manhole, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 0586750 | Type “C” Catch Basin Top, per Each, the price of: ($ ) | Each | 14 | $_______________ |
| 0586752 | Type "C" Catch Basin Top Double Grate Type 2, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 0586760 | Type “C-L” Catch Basin Top, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 0601109A | Class “A” Concrete for Retaining Walls, per CY, the price of: ($ ) | CY | 825 | $_______________ |
| 0601082A | 7’ x 7’ Pre-cast Concrete Box Culvert, per LF, the price of: ($ ) | LF | 120 | $_______________ |
| 0605391A | Structural Steel – Watermain Brackets, per Each, the price of: ($ ) | Each | 8 | $_______________ |
| 0605003A | Masonry Facing for Retaining Walls and Culvert Wing Walls, per SY, the price of: ($ ) | SY | 3,500 | $_______________ |
| 0607001 | Reset Masonry Wall, per CY, the price of: ($ ) | CY | 80 | $_______________ |
| 0612994 | Concrete Cylinder Curing Box, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 0653001 | Clean Existing Catch Basin, per Each, the price of: ($ ) | Each | 20 | $_______________ |
| 0653100 | Clean Existing Culvert (12”-42” Diameter), per LF, the price of: ($ ) | LF | 300 | $_______________ |
| 0686200.3 | 30” R.C. Pipe (Class V) – 0-10’deep, per LF, the price of: ($ ) | LF | 10 | $_______________ |
| 0686200.60 | 6” Perforated Polyvinyl Chloride Pipe, per LF, the price of: ($ ) | LF | 850 | $_______________ |
| 0686200.12 | 12” Polyvinyl Chloride Pipe, per LF, the price of: ($ ) | LF | 1,100 | $_______________ |
| 0686200.15 | 15” Polyvinyl Chloride Pipe, per LF, the price of: ($ ) | LF | 1,500 | $_______________ |
| 0686200.18 | 18” Polyvinyl Chloride Pipe, per LF, the price of: ($ ) | LF | 600 | $_______________ |
| 0815001 | Bituminous Concrete Lip Curb, per LF, the price of: ($ ) | LF | 19,800 | $_______________ |
| 0822001 | Temporary Pre-cast Concrete Barrier Curb, per LF, the price of: ($ ) | LF | 225 | $_______________ |
| 095007 | Reset Stone Wall, per LF, the price of: ($ ) | LF | 565 | $_______________ |
| 0910310 | Metal Beam Rail R-B MASH, per LF, the price of: ($ ) | LF | 1,050 | $_______________ |
| 0911001 | Metal Beam Rail Anchor Type II, per Each, the price of: ($ ) | Each | 14 | $_______________ |
| 0910007 | Metal Beam Rail Attachment Assembly, per Each, the price of: ($ ) | Each | 4 | $_______________ |
| 0912510 | Remove Existing Guide Railing, per LF, the price of: ($ ) | LF | 480 | $_______________ |
| 0912001 | Chain Link Fence (42” high), per LF, the price of: ($ ) | LF | 750 | $_______________ |
| 0921005 | Concrete Sidewalk Ramp, per SY, the price of: ($ ) | SF | 1,087 | $_______________ |
| 0921039 | Detectable Warning Strip, per Each, the price of: ($ ) | Each | 16 | $_______________ |
| 0922001 | Bituminous Concrete Sidewalk, per SY, the price of: ($ ) | SY | 17,215 | $_______________ |
| 0922501 | Bituminous Concrete Driveway, per SY, the price of: ($ ) | SY | 2,585 | $_______________ |
| 0922502 | Heavy Duty Bituminous Concrete Driveway, per SY, the price of: ($ ) | SY | 100 | $_______________ |
| 0942001 | Calcium Chloride for Dust Control, per TON, the price of: ($ ) | Ton | 30 | $_______________ |
| 0943002 | Water for Dust Control, per M.Gal, the price of: ($ ) | M. Gal | 1,000 | $_______________ |
| 0950001A | Reset Belgium Block Apron, per SY, the price of: ($ ) | SF | 100 | $_______________ |
| 0950005A | Reset Stone Curb, per LF, the price of: ($ ) | LF | 50 | $_______________ |
| 0944001 | Furnishing and Placing Topsoil, per SY, the price of: ($ ) | SY | 8,500 | $_______________ |
| 0950019A | Turf Establishment, per SY, the price of: ($ ) | SY | 8,500 | $_______________ |
| 0950039 | Erosion Control Matting Type D, per SY, the price of: ($ ) | SY | 260 | $_______________ |
| 09690060A | Construction Field Office, Small, per Month, the price of: ($ ) | Month | 20 | $_______________ |
| 0970006A | Traffic Person (Municipal Police Officer), per Est., the price of: Five Hundred Thousand and 00/100 ($ $500,000.00 ) | Est. | 1 | $500,000.00 |
| 0970060A | Traffic Person (Uniformed Flagger), per Hour, the price of: ($ ) | SY | 260 | $_______________ |
| 0971001 | Maintenance and Protection of Traffic, per LS, the price of: ($ ) | LS | 1 | $_______________ |
| 0975004 | Mobilization and Project Closeout, per LS, the price of: ($ ) | LS | 1 | $_______________ |
| 0976002 | Barricade Warning Lights – High Intensity, per day, the price of: ($ ) | Day | 1,000 | $_______________ |
| 0977001 | Traffic Cone, per Each, the price of: ($ ) | Each | 100 | $_______________ |
| 0978002 | Traffic Drum, per Each, the price of: ($ ) | Each | 50 | $_______________ |
| 0979003 | Construction Barricade Type-III, per Each, the price of: ($ ) | Each | 4 | $_______________ |
| 0980001A | Construction Staking, per LS, the price of: ($ ) | LS | 1 | $_______________ |
| 1001001 | Trenching and Backfilling, per LF, the price of: ($ ) | LF | 790 | $_______________ |
| 1001004 | Rock In Trench (0-4’ deep), per CY, the price of: ($ ) | CY | 10 | $_______________ |
| 1002015 | Rock In Foundation Excavation, per VF, the price of: ($ ) | VF | 10 | $_______________ |
| 1002202 | Traffic Control Foundation – Mast Arm, per Each, the price of: ($ ) | Each | 2 | $_______________ |
| 1002203 | Traffic Control Foundation – Pedestal Type 1, per Each, the price of: ($ ) | Each | 3 | $_______________ |
| 1002208 | Traffic Control Foundation – Controller Type IV, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1008015 | 2” Rigid Metal Conduit - Surface, per LF, the price of: ($ ) | LF | 40 | $_______________ |
| 1008115 | 2” Rigid Metal Conduit - In Trench, per LF, the price of: ($ ) | LF | 410 | $_______________ |
| 1008215 | 2” Rigid Metal Conduit – Under Roadway, per LF, the price of: ($ ) | LF | 380 | $_______________ |
| 1010021 | Concrete Handhole, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1010001 | Concrete Handhole – Type II, per Each, the price of: ($ ) | Each | 5 | $_______________ |
| 1010054 | Cast Iron Handhole Cover Type II, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1017032A | Service (metered), per Lump Sum, the price of: ($ ) | LS | 1 | $_______________ |
| 1102002A | 8’ Aluminum Pedestal, per Each, the price of: ($ ) | Each | 3 | $_______________ |
| 1104033A | 40’ Steel Mast Arm Assembly, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1105037A | 45’ Steel Mast Arm Assembly, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1105105 | 1 Way, 5 Section Mast Arm Traffic Signal, per Each, the price of: ($ ) | Each | 2 | $_______________ |
| 1105103A | 1 Way, 3 Section Mast Arm Traffic Signal, per Each, the price of: ($ ) | Each | 3 | $_______________ |
| 1106003A | 1 Way Pedestrian Signal Pedestal Mount, per Each, the price of: ($ ) | Each | 2 | $_______________ |
| 1106004A | 2 Way Pedestrian Signal Pedestal Mount, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1107011A | Accessible Pedestrian Signal, per Each, the price of: ($ ) | Each | 3 | $_______________ |
| 1108115A | Full Actuated Controller 8 Phase, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1112288A | IP Video Detection Camera Assembly, per Each, the price of: ($ ) | Each | 2 | $_______________ |
| 1113014 | 3 Conductor No. 8 AWG Type SE Style THW, per LF, the price of: ($ ) | LF | 100 | $_______________ |
| 1113102 | 5 Conductor No. 14 Cable, per LF, the price of: ($ ) | LF | 700 | $_______________ |
| 1113103 | 7 Conductor No. 14 Cable, per LF, the price of: ($ ) | LF | 650 | $_______________ |
| 1113104 | 9 Conductor No. 14 Cable, per LF, the price of: ($ ) | LF | 400 | $_______________ |
| 1113725A | T23 AWG 4 Twisted Pair Category 6 Cable, per LF, the price of: ($ ) | LF | 600 | $_______________ |
| 1118051A | Temporary Signalization Site No. 1, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1111201A | Temporary Detection Site No. 1, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1111407A | Camera Video Detection System, per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1111600A | Extension Bracket, per Each, the price of: ($ ) | Each | 2 | $_______________ |
| 1206023A | Removal and Relocation of Existing Signs, per Lump Sum, the price of: ($ ) | LS | 1 | $_______________ |
| 1208931A | Sign Face – sheet Aluminum (Type IX Retroreflective Sheeting), per SF, the price of: ($ ) | SF | 75 | $_______________ |
| 1208932A | Sign Face – sheet Aluminum (Type IV Retroreflective Sheeting), per SF, the price of: ($ ) | SF | 300 | $_______________ |
| 1209005 | Temporary 4” White Painted Pavement Markings, per LF, the price of: ($ ) | LF | 8,000 | $_______________ |
| 1210101 | 4” White Epoxy Resin Pavement Marking, per LF, the price of: ($ ) | LF | 15,000 | $_______________ |
| 1210102 | 4” Yellow Epoxy Resin Pavement Marking, per LF, the price of: ($ ) | LF | 19,200 | $_______________ |
| 1210105 | Epoxy Resin Legend, Arrows and Markings, per SF, the price of: ($ ) | SF | 1,500 | $_______________ |
| 1220027 | Construction Signs, per SF, the price of: ($ ) | SF | 400 | $_______________ |
| 1302050 | Reset Valve Boxes, per Each, the price of: ($ ) | Each | 31 | $_______________ |
| 1801002 | Repair of Impact Attenuation System Type A Module 700 lb., per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1801003 | Repair of Impact Attenuation System Type A Module 1,400 lb., per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1801004 | Repair of Impact Attenuation System Type A Module 2,100 lb., per Each, the price of: ($ ) | Each | 1 | $_______________ |
| 1807012 | Temporary Impact Attenuation System Type A Module 700 lb., per Each, the price of: ($ ) | Each | 4 | $_______________ |
| 1807013 | Temporary Impact Attenuation System Type A Module 1400 lb., per Each, the price of: ($ ) | Each | 20 | $_______________ |
| 1807014 | Temporary Impact Attenuation System Type A Module 2100 lb., per Each, the price of: ($ ) | Each | 8 | $_______________ |
| 1807101A | Relocation of Temporary Impact Attenuation System Type A, per Each, the price of: ($ ) | Each | 8 | $_______________ |

TOTAL AMOUNT OF BID – (A) LOTCIP Funds Participating

_______________________________________________________ ____________________

Dollars (in words)

($	____________________________________________________________________)

(In figures)

| Strobel Road Reconstruction Project – Non-Participating Pay Items |
| --- |
| Item Number | Item Name and Unit Bid Prices Written in Words and Figures | Units | Estimated Quantity | Total Amount of Item (in figures) |
| 0949000 | Furnishing and Placing Wood Chip Mulch, per SY, the price of: ($ ) | SY | 200 | $_______________ |
| 0949148 | Furnishing and Placing CORNUS RUTGERS PINK, STELLAR PINK DOGWOOD, 10-15’ HT. B.B., per Each, the price of: ($ ) | Each | 12 | $_______________ |
| 0949881 | Furnishing and Placing LIQUIDAMBAR STYRACIFUA AMERICAN SWEETGUM. 3 ½”-4” CAL. B.B. per Each, the price of: ($ ) | Each | 7 | $_______________ |
| 0949609 | Furnishing and Placing PICEA ABIES, NORWAY SPRUCE, 6- - 8’ HT. B.Bl, per Each, the price of: ($ ) | Each | 27 | $_______________ |
| 0944001 | Furnishing and Placing PICEA OMORIKA, SERBIAN SPRUCE, 6- - 8’ HT. B.B., per Each, the price of: ($ ) | Each | 11 | $_______________ |

TOTAL AMOUNT OF BID – (B) Non-Participating

_______________________________________________________ ____________________

Dollars (in words)

($	____________________________________________________________________)

(In figures)

TOTAL AMOUNT OF BID (A+B) – Participating and Non-Participating

_______________________________________________________ ____________________

Dollars (in words)

($	____________________________________________________________________)

(In figures)

THE QUANTITIES IN THIS BID FORM ARE FOR PURPOSES OF ILLUSTRATION ONLY. THE FINAL QUANITIES WILL BE DETERMINED BY THE ACTUAL WORK COMPLETED.

PROPOSAL (continued)

Respectfully submitted,

________________________________________________			________________________________________________

Company Name														By (Signature)

________________________________________________			________________________________________________

Address																Print Name

_________________________________________________			________________________________________________

Address																Title

(SEAL-if proposal is by a corporation)

Note: Insert Proposer's name. If a corporation, give the State of Incorporation using the phrase, "A corporation organized under the laws of

____________________________, composed of officers as follows:

____________________________________			____________________________________

President					 							Secretary

____________________________________			____________________________________

Vice President											Treasurer

If a partnership, give names of partners, using also the phrase, "co-partners trading and doing business under the firm name and style of______________________________, composed of partners as follows:

____________________________________________________________________________________________________EMAIL

END OF GENERAL BID: